## Slide 1
Project Description:
PCB with 2 cameras and STM32 microcontroller. Both cameras are the same model. The software runs in a loop for ever. In the loop, an image from one camera is captured and transmitted out of the user specified output device (USB or UART). The next time the loop runs, the other camera is used.
The user selects the output device (UART or USB) via a selectable switch on the PCB
Output Packet
The output of each image to USB or UART includes a header. There is a header transmitted before each image. The header identifier begins with EZIMG for one camera, and EZIRC for the other camera. Following the header identifier are 4 bytes representing the image size. And finally, the image data is sent.
Header Examples
EZIMG<4 bytes image size><image data>
EZIRC<4 bytes image size><image data>

## Slide 2
Experience Requirements:
STM32F407VGT6 Microcontroller
STD Peripheral or HAL
DCMI
DMA
UART
USB

## Slide 3
Overview:
Existing code works with UART. Now we’d like to add USB (user selectable by a switch on GPIOA_3)
we’re okay with code being ported to work with HAL rather than STDPERIPHERAL (up to you)
PCB has 2 i2c cameras (i2c1 & i2c2)
STM32 has 1 DMCI interface
The DMCI of each camera is passed through a TS3DV20812 switching chip controlled by GPIOE_4
Program Start:
Init the peripherals and DMA, etc.
Get the user output selected interface from GPIOA_3 switch
Init the user selected output interface (high is UART and low is USB)
Init each camera. If i2c fails to initialize the camera, transmit the error message using the appropriate header of the failed camera (0 EZIRC and 1 is EZIMG)
Program Loop:
The GPIOE_4 alternates between each camera for each irritation of the loop
The camera dumps its data into the DMA buffer
Waits until DCMI has completed (while ((DCMI->CR & DCMI_CR_CAPTURE) != 0))
Send the data in the buffer to the specified output interface. The output interface is user selectable with GPIOA_3 switch on bootup. (high is UART and low is USB)

## Slide 4
DCMI
Camera 1
Camera 2
Switching IC
I2C1
I2C2
GPIO
DMA
Alternate Between Camera
USB or UART selected?
Send DMA Buffer Out UART with RTS
Send DMA Buffer Out USB